## Slide 1: NT101-Network Security
Ngoc-Tu Nguyen, PhD
tunn@uit.edu.vn
Week 03 Computer Networking: a review

## Slide 2: Outline
Motivations
Protocol layers
Vulnerabilities
Expoint and attacks
Generic countermeasures

## Slide 3: The Internet

## Slide 4: The Internet: the network of networks
Internet
mobile network
home network
enterprise
network
na
P
local or regional ISP
er
co pro
netwo
Billions of connected computing devices:
hosts = end systems
running network apps at Internet’s “edge”
Packet switches: forward packets (chunks of data)
routers, switches
Communication links
fiber, copper, radio, satellite
transmission rate: bandwidth
Networks
collection of devices, routers, links: managed by an organization

## Slide 5: The Internet: network of networks
Internet: “network of networks”
  Interconnected ISPs
home network
enterprise
network
na
P
local or regional ISP
er
HTTP
Ethernet
co pro
netwo
Skype
IP
WiFi
mobile network 4G
TCP
Streaming video
protocols are everywhere
  control sending, receiving of messages
  e.g., HTTP (Web), streaming video, Skype, TCP, IP, WiFi, 4G, Ethernet
Internet standards
  RFC: Request for Comments
  IETF: Internet Engineering Task Force

## Slide 6: The Internet: a “services” view
mobile network
home network
enterprise
network
na
P
local or regional ISP
er
co pro
netwo
HTTP
Skype
Streaming video
Infrastructure that provides services to applications:
  Web, streaming video, multimedia teleconferencing, email, games, e- commerce, social media, inter- connected appliances, …
provides programming interface
to distributed applications:
  “hooks” allowing sending/receiving apps to “connect” to, use Internet transport service
  provides service options, analogous to postal service

## Slide 7: Internet history
2005-present: scale, SDN, mobility, cloud
aggressive deployment of broadband home access (10-100’s Mbps)
2008: software-defined networking (SDN)
increasing ubiquity of high-speed wireless access: 4G/5G, WiFi
service providers (Google, FB, Microsoft) create their own networks
  bypass commercial Internet to connect “close” to end user, providing
“instantaneous” access to social media, search, video content, …
enterprises run their services in “cloud” (e.g., Amazon Web Services, Microsoft Azure)
rise of smartphones: more mobile than fixed devices on Internet (2017)
~18B devices attached to Internet (2017)

## Slide 8: A closer look at Internet structure
mobile network
na P
local or regional ISP
home network co
pro
netwo er
enterprise
network
Network edge:
hosts: clients and servers
servers often in data centers

## Slide 9: A closer look at Internet structure
mobile network
na P
local or regional ISP
home network co
pro
netwo er
enterprise
network
Network edge:
 hosts: clients and servers
 servers often in data centers
Access networks, physical media:
edge router
wired, wireless communication links

## Slide 10: A closer look at Internet structure
Network edge:
 hosts: clients and servers
 servers often in data centers
Access networks, physical media:
wired, wireless communication links
Network core:
interconnected routers
network of networks
mobile network
home network
enterprise
network
na
P
local or regional ISP
er
co pro
netwo

## Slide 11: Two key network-core functions
Forwarding:
aka “switching”
local action: move arriving packets from router’s input link to appropriate
router output link
1
2
3
0111
destination address in arriving packet’s header
local forwarding table
local forwarding table | 
header value | output link
0100 | 3
0101 | 2
0111 | 2
1001 | 1
Routing:
global action: determine source- destination paths taken by packets
routing algorithms
routing algorithm

## Slide 12: routing

## Slide 13: forwarding
forwarding

## Slide 14: Packet delay: four sources transmission
dproc: nodal processing
check bit errors
determine output link
typically < microsecs
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
nodal
processing queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B

## Slide 15: Packet delay: four sources
propagation
nodal
processing queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
dtrans: transmission delay:
L: packet length (bits)
R: link transmission rate (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
d and d
trans prop
very different

## Slide 16: Protocol stack
NT101 – Network Security

## Slide 17: Why layering?
Approach to designing/discussing complex systems:
explicit structure allows identification, relationship of system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change in layer's service implementation: transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system

## Slide 18: Layered Internet protocol stack
application: supporting network applications
  HTTP, IMAP, SMTP, DNS
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits “on the wire”
link
application
network
transport
physical
application
transport
network
link
physical

## Slide 19: Services, Layering and Encapsulation
source
application
transport
network
link
physical
destination
application
transport
network
link
physical
Application exchanges messages to implement some application service using services of transport layer
Ht M
Transport-layer protocol transfers M (e.g., reliably) from one process to another, using services of network layer
transport-layer protocol encapsulates application-layer message, M, with transport layer-layer header Ht to create a transport-layer segment
  Ht used by transport layer protocol to implement its service
M

## Slide 20: Services, Layering and Encapsulation
source
application
transport
network
link
physical
destination
M
application
transport
network
link
physical
Ht M
Transport-layer protocol transfers M (e.g., reliably) from one process to another, using services of network layer
Hn Ht M
Network-layer protocol transfers transport-layer segment [Ht | M] from one host to another, using link layer services
network-layer protocol encapsulates transport-layer segment [Ht | M] with network layer-layer header Hn to create a network-layer datagram
  Hn used by network layer protocol to implement its service

## Slide 21: Services, Layering and Encapsulation
source
Ht
M
application
transport
network
link
physical
destination
M
application
transport
network
link
physical
Link-layer protocol transfers datagram [Hn| [Ht |M] from
host to neighboring host, using network-layer services
link-layer protocol encapsulates network datagram [Hn| [Ht |M], with link-layer header Hl to create a link-layer frame
Hl | Hn | Ht | M
Hn Ht M
Network-layer protocol transfers transport-layer segment [Ht | M] from one host to another, using link layer services

## Slide 22: Services, Layering and Encapsulation
source
application
transport
network
link
physical
destination
application
transport
network
link
physical
Ht
M
M
Hn | Ht | M
Hl | Hn | Ht | M
M
Hn Ht
Ht M
M
message
segment
datagram
frame
Hl | Hn | Ht | M

## Slide 23: Encapsulation: an end-end view
network
link physical
application
transport
network
link
physical
transport network
link physical
source
application
Hn
M
segment
Ht
datagram
destination
 | Hn | Ht | M
Hl | Hn | Ht | M
Ht
M
M
Hl | Hn | Ht | M
Hn | Ht | M
Ht
Hn
M
Hl
Hn Ht M
router
message
M
Ht
M
Hn Ht
frame
link physical
switch

## Slide 24: ISO/OSI reference model
Two layers not found in Internet protocol stack!
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
network
link
physical
The seven layer OSI/ISO reference model

## Slide 25: Network Security At a glance

## Slide 26: Network security
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  security considerations in all layers!
We now need to think about:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks

## Slide 27: What is network security?
confidentiality: only sender, intended receiver should “understand” message contents
sender encrypts message
receiver decrypts message
authentication: sender, receiver want to confirm identity of each other
message integrity: sender, receiver want to ensure message not altered (in transit, or afterwards) without detection
access and availability: services must be accessible and available to users

## Slide 28: Friends and enemies: Alice, Bob, Trudy
well-known in network security world
Bob, Alice (lovers!) want to communicate “securely”
Trudy (intruder) may intercept, delete, modify/add messages
secure sender
secure
receiver
channel data, control
messages
data
data
Alice
Bob
Trudy

## Slide 29: Friends and enemies: Alice, Bob, Trudy
Who might Bob and Alice be?
… well, real-life Bobs and Alices!
Web browser/server for electronic transactions (e.g., on-line purchases)
on-line banking client/server
DNS servers
BGP routers exchanging routing table updates
other examples?

## Slide 30: There are bad guys (and girls) out there!
Q: What can a “bad guy” do?
A: A lot!
eavesdrop: intercept messages
actively insert messages into connection
impersonation: can fake (spoof) source address in packet (or any field in packet)
hijacking: “take over” ongoing connection by removing sender or receiver, inserting himself in place
denial of service: prevent service from being used by others (e.g., by overloading resources)

## Slide 31: Bad guys: packet interception
packet “sniffing”:
broadcast media (shared Ethernet, wireless)
promiscuous network interface reads/records all packets (e.g., including passwords!) passing by
A
C
src:B dest:A
payload
B
Wireshark software used for our end-of-chapter labs is a (free) packet-sniffer Alternatives: tcpdump, scapy,…

## Slide 32: Bad guys: fake identity
IP spoofing: injection of packet with false source address
A
B
C
src:B
dest:A
payload
 Looking ahead: More deeply analysis of Sniffing and Spoofing in the next lecture

## Slide 33: Bad guys: denial of service
target
Denial of Service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
1. select target
break into hosts around the network (see botnet)
send packets to target
from compromised hosts

## Slide 34: Lines of defense:
authentication: proving you are who you say you are
  cellular networks provides hardware identity via SIM card; no such hardware assist in traditional Internet
confidentiality: via encryption
integrity checks: digital signatures prevent/detect tampering
access restrictions: password-protected VPNs
firewalls: specialized “middleboxes” in access and core networks:
off-by-default: filter incoming packets to restrict senders, receivers, applications
detecting/reacting to DOS attacks
 lots more on network defense (throughout Lecture 11)

## Slide 35: For next time…
NT101 – Network Security
Winter 2020
Looking ahead
Ready for next class:
Tentative topic: Packet Sniffing and Spoofing
Reading and practicing (in advance):
  SEED book, Chapter 15
    Refs: https://www.handsonsecurity.net/resources.html
  SEED Lab: Packet Sniffing and Spoofing Lab
    Refs: https://seedsecuritylabs.org/Labs_16.04/Networking/Sniffing_Spoofing/
38

## Slide 36: Authentication: a case study
Goal: Bob wants Alice to “prove” her identity to him Protocol ap1.0: Alice says “I am Alice”
failure scenario??
“I am Alice”

## Slide 37: Authentication: issues
Goal: Bob wants Alice to “prove” her identity to him Protocol ap1.0: Alice says “I am Alice”
in a network, Bob can not “see” Alice, so Trudy simply declares herself to be Alice
“I am Alice”

## Slide 38: Authentication: another try
Goal: Bob wants Alice to “prove” her identity to him
Protocol ap2.0: Alice says “I am Alice” in an IP packet containing her source IP address
“I am Alice”
Alice’s IP address
failure scenario??

## Slide 39: Authentication: another try
Goal: Bob wants Alice to “prove” her identity to him
Protocol ap2.0: Alice says “I am Alice” in an IP packet containing her source IP address
“I am Alice”
Alice’s IP address
Trudy can create a packet “spoofing”
Alice’s address

## Slide 40: Authentication: a third try
Alice’s IP addr | Alice’s password | “I am Alice”
Goal: Bob wants Alice to “prove” her identity to him
Protocol ap3.0: Alice says “I am Alice” Alice says “I am Alice” and sends her secret password to “prove” it.
failure scenario??
Alice’s IP addr
OK

## Slide 41: Authentication: a third try
Alice’s IP addr | Alice’s password | “I am Alice”
Alice’s
IP addr
OK
“I am Alice”
Alice’s
IP addr
Alice’s
password
Goal: Bob wants Alice to “prove” her identity to him
Protocol ap3.0: Alice says “I am Alice” Alice says “I am Alice” and sends her secret password to “prove” it.
replay attack: Trudy records Alice’s packet and later
plays it back to Bob

## Slide 42: Authentication: a modified third try
Alice’s IP addr | encrypted password | “I am Alice”
Goal: Bob wants Alice to “prove” her identity to him
Protocol ap3.0: Alice says “I am Alice” Alice says “I am Alice” and sends her encrypted secret password to “prove” it.
failure scenario??
Alice’s IP addr
OK

## Slide 43: Authentication: a modified third try
Alice’s IP addr | encrypted password | “I am Alice”
Alice’s
IP addr
OK
“I am Alice”
Alice’s
IP addr
encrypted
password
Goal: Bob wants Alice to “prove” her identity to him
Protocol ap3.0: Alice says “I am Alice” Alice says “I am Alice” and sends her encrypted secret password to “prove” it.
replay attack still works: Trudy records Alice’s packet
and later plays it back to Bob

## Slide 44: Authentication: a fourth try
Failures, drawbacks?
KA-B(R)
Goal: avoid replay attack
nonce: number (R) used only once-in-a-lifetime
protocol ap4.0: to prove Alice “live”, Bob sends Alice nonce, R
Alice must return R, encrypted with shared secret key
“I am Alice”
R
Bob know Alice is live, and
only Alice knows key to encrypt nonce, so it must be Alice!

## Slide 45: Authentication: ap5.0
ap4.0 requires shared symmetric key - can we authenticate using public key techniques?
ap5.0: use nonce, public key cryptography
“I am Alice”
R
KA (R)
-
Send me your public key
A
K+
Bob computes
-
A (KA(R)) = R’ ?= R
K +
Public key / secret key
K- /K+

## Slide 46: Authentication: ap5.0 – there’s still a flaw! man (or woman) in the middle attack: Trudy poses as Alice (to Bob) and as Bob (to Alice)
I am Alice
I am Alice
Send me your public key
T
m = K (K T(m))
- +
Trudy recovers m:
sends m to Alice encrypted with Alice’s public key
K T(R)
R-
T
K+
T
K (K T(R)) = R,
+ -
Bob computes
authenticating Trudy as Alice
R
A
K - (R)
+
Send me your public key
KA
K (m)
+
T
Bob sends a personal message, m to Alice
KA(m)
+
A
A
m = K- (K+(m))
Trudy recovers Bob’s m:
and she and Bob meet a week later in person and discuss m, not knowing Trudy knows m
?
Where are
mistakes
made here?

## Slide 47: Authentication: modified ap5.0
ap4.0 requires shared symmetric key - can we authenticate using public key techniques?
ap5.0: use nonce, public key cryptography
“I am Alice”
R
KA (R)
-
Bob computes
-
A (KA(R)) = R’ ?= R
K +
Public key / secret key
K- /K+
K+
Bob know Alice’s public key:
How ditribute Alice’s public?

## Slide 48: Need for certified public keys
motivation: Trudy plays pizza prank on Bob
  Trudy creates e-mail order:
Dear Pizza Store, Please deliver to me four pepperoni pizzas. Thank you, Bob
  Trudy signs order with her private key
  Trudy sends order to Pizza Store
  Trudy sends to Pizza Store her public key, but says it’s Bob’s public key
  Pizza Store verifies signature; then delivers four pepperoni pizzas to Bob
  Bob doesn’t even like pepperoni

## Slide 49: Public key Certification Authorities (CA)
certification authority (CA): binds public key to particular entity, E
entity (person, website, router) registers its public key with CE provides “proof of identity” to CA
  CA creates certificate binding identity E to E’s public key
  certificate containing E’s public key digitally signed by CA: CA says “this is E’s public key”
Bob’s identifying information
KB
+
certificate for Bob’s public key, signed by CA
Bob’s
public
key KB
+
digital signature (encrypt)
CA’s
key
CA
private K -

## Slide 50: Public key Certification Authorities (CA)
Bob’s public key
K B
+
KB
+
when Alice wants Bob’s public key:
  gets Bob’s certificate (Bob or elsewhere)
  apply CA’s public key to Bobʼs certificate, get Bob’s public key
CA’s
key
CA
public K+
digital signature (decrypt)