## Slide 1: NT101-Network Security
Ngoc-Tu Nguyen, PhD
tunn@uit.edu.vn
Week 08-09: Network layer security

## Slide 2: Outline
ARP poisoning and MiMA attacks (review)
The Role of the IP layer
IP Header
IP Fragmentation and Attacks
Routing
ICMP and Attacks

## Slide 3
network
link physical
application
transport
network
link
physical
transport network
link physical
source
application
Hn
M
segment
Ht
datagram
destination
 | Hn | Ht | M
Hl | Hn | Ht | M
Ht
M
M
Hl | Hn | Ht | M
Hn | Ht | M
Ht
Hn
M
Hl
Hn Ht M
IP router
message
M
Ht
M
Hn Ht
frame
link physical
switch
Motivations
Hl | Hn | Ht | M
Secure Routing
Seccure hop-by-hop
Routing!
next hop?
next hop?
next hop?
MAC?
Intermediary devices

## Slide 4
ARP Cache Poisoning
MAC Layer attack
How to cause ARP to update its cache?
 Sending out
ARP Request
ARP Reply
ARP Gratituous (broadcast response)
ARP cache table!
IP U:MAC U
IP H:MAC H
IP G:MAC G
ARP table:
IP H:MAC M
M
ARP table:
IP H:MAC M

## Slide 5: ARP Poisoning Attack code example
Before
After
Victim IP: 10.102.20.177
MAC: 00:50:56:a8:0e:77
Target: 10.102.20.178
MAC: 00:50:56:a8:1a:d3
LAN
ARP cache table
IP: 10.102.20.177 MAC: 00:50:56:a8:0e:77
Attacker
IP: 10.102.20.154
IP: 10.102.20.177 MAC: aa:bb:cc:dd:ee:ff
A
B
M
MAC: aa:bb:cc:dd:ee:ff

## Slide 6: ARP Poisoning Attack code example
Spoofing ARP Request
Attacker IP: 10.102.20.154
Target: 10.102.20.178 – MAC: 00:50:56:a8:1a:d3 Victim IP: 10.102.20.177 – MAC: 00:50:56:a8:0e:77
Sending spoofed ARP request directly to Victim (Unicast)
When A receives this, it is going to see that 10.102.20.177 is mapped to this fake MAC
 add to ARP cache.
Before
After

## Slide 7: ARP Poisoning Attack code example Spoofing ARP Gratuitous and Reply
ARP Gratuitous
ARP Reply

## Slide 8: Remind: Man-in-the-middle attack Diffie-Hellman key exchange
a
A ← ga mod p
Alice
Bob
b
gb mod p  B
A
B
KA ←Ma mod p = gma mod p
B
K ←Mb mod p = gmb mod p
Share a prime number p and g < p (g is a primmitive root of p)
Micheal
m
M
M
I love you
E(KA, M)
» M m
: + (
D(KA, M)
I love you
I hate you
E(KB, M)
x * #
@ $ (
D(KB, M)
I hate you
M ← gm mod p
K1 = Am mod p = gam mod p = KA
K2 = Bm mod p = gbm mod p = KB

## Slide 9: Main-in-the-Middle (MITM) Attack Using ARP cache poisoning
(can see or modify)
Attack idea:
M has to be on the same network as A and B
 try to cache poison A and B’s cache
When A is sending a packet to B
IP header is still: IP A  IP B
MAC address: MAC A  MAC M
 B can still get A’s packet but will drop it!
Micheal
Alice
Bob
MAC M
MAC M
What’s going to happen when that frame arrives at M?
ARP table
IP: IP B
MAC: MAC B
 MAC M
ARP table
IP: IP A
MAC: MAC A
 MAC M

## Slide 10: Main-in-the-Middle (MITM) Attack (cont.) Using ARP cache poisoning
(can see or modify)
Micheal
Alice
Bob
MAC M
MAC M
DHCP
UDP
IP
Eth
Phy
M
When that frame arrives at M:
dstIP = IP B
ARP table
IP: IP B
MAC: MAC B
 MAC M
ARP table
IP: IP A
MAC: MAC A
 MAC M
 2 scenarios:
If M is configured as a router
 Relay that packet to B
If M is configured as a hosts
 Drop the packet
So, what we need to do next?

## Slide 11: Main-in-the-Middle (MITM) Attack Using ARP cache poisoning
Alice
Bob
MAC M
MAC M
ARP table
IP: IP B
MAC: MAC B
 MAC M
ARP table
IP: IP A
MAC: MAC A
 MAC M
Micheal
(can see or modify)
IP Forwarding = 0
Then, make some changes and send it out!
 B gets the modified packet!

## Slide 12: source
network
link physical
application
transport
network
link
physical
application transport network
link physical
Packet’s Traversal
Hn
M
segment
Ht
datagram
destination
 | Hn | Ht | M
Hl | Hn | Ht | M
Ht
M
M
Hl | Hn | Ht | M
Hn | Ht | M
Ht
Hn
M
Hl
Hn Ht M
router
message
M
Ht
M
Hn Ht
frame
link physical
switch
Which ouput link?
Which ouput link?
ARP table

## Slide 13: Network-layer services and protocols
transport segment from sending to receiving host
  sender: encapsulates segments into datagrams, passes to link layer
  receiver: delivers segments to transport layer protocol
network layer protocols in every Internet device: hosts, routers
routers:
  examines header fields in all IP datagrams passing through it
  moves datagrams from input ports to output ports to transfer datagrams along end-end path
mobile network
enterprise
network
na
P
er
application
transport
network
link
physical
application
transport
network
link
physical
network
link physical
network
link
physical
network
link
physical
network
link physical
network
link
physical

## Slide 14: Packet Forwarding and Routing
A
B
203.105.8.11
129.9.124.1
129.10.5.5
129.10.1.25
129.10.1.1
A send a package to C?
C
Need IP header!

## Slide 15: Two key network-layer functions
forwarding
routing
analogy: taking a trip
forwarding: process of getting through single interchange
routing: process of planning trip from source to destination
network-layer functions:
forwarding: move packets from a router’s input link to appropriate router output link
routing: determine route taken by packets from source to destination
  routing algorithms

## Slide 16: Network layer: data plane, control plane
0111
Data plane:
local, per-router function
determines how datagram arriving on router input port is forwarded to router output port
values in arriving packet header
Control plane
network-wide logic
determines how datagram is routed among routers along end- end path from source host to destination host
two control-plane approaches:
  traditional routing algorithms:
    implemented in routers
  software-defined networking (SDN):
    implemented in (remote) servers

## Slide 17: Per-router control plane Individual routing algorithm components in each and every router interact in the control plane
Routing Algorithm
data plane
control plane
Local forwarding table
header | output
0100 | 3
0110 | 2
0111 | 2
1001 | 1
1
2
0111
values in arriving packet header
3

## Slide 18: Software-Defined Networking (SDN) control plane Remote controller computes, installs forwarding tables in routers
control plane
data plane
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving packet header

## Slide 19: Network Layer: Internet
host, router network layer functions:
network
layer
transport layer: TCP, UDP
Path-selection IP protocol algorithms: • datagram format addressing implemented in • packet handling conventions routing protocols forwarding (OSPF, BGP) table ICMP protocol SDN controller • error reporting router “signaling”
link layer
physical layer

## Slide 20: IP Datagram format
IP header
ver
length
32 bits
payload data (variable length, typically a TCP or UDP segment)
16-bit identifier
header
checksum
time to live
source IP address
head. type of len service
flgs
fragment offset
upper layer
destination IP address
options (if any)
IP protocol version number (4 bits)
header length(bytes) (4 bits)
upper layer protocol (e.g., TCP or UDP)
total datagram
“type” of service:
diffserv (0:5)
ECN (6:7)
TTL: remaining max hops
(decremented at each router)
20 bytes of TCP
20 bytes of IP
 = 40 bytes + app layer overhead for TCP+IP
overhead
route taken
it destination IP address
timestamp, record
length (bytes) (16 bits)
fragmentation/ reassembly
header checksum
32-bit source IP address
Maximum length: 64K bytes
32-b Typically: 1500 bytes or less
e.g., Can we overflow this value?

## Slide 21: IP header An example
21

## Slide 22: Time-to-Live and How Traceroute works ICMP Protocol
when ICMP message arrives at source: record RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
3 probes
3 probes
3 probes
source sends sets of UDP segments to destination
1st
set has TTL =1, 2nd set has TTL=2, etc.
datagram in nth set arrives to nth router:
  router discards datagram and sends source ICMP message (type 11, code 0)
  ICMP message possibly includes name of router & IP address

## Slide 23: Traceroute example ICMP Protocol
<< What happened here?
Why we need to set TTL?

## Slide 24
NT101 – Network Security
IP Fragmentation
Attack

## Slide 25: IP fragmentation/reassembly
large IP datagram divided (“fragmented”) within net
one datagram becomes several datagrams
“reassembled” only at destination
IP header bits used to identify, order related fragments
The need for Fragmentation
network links have MTU (max. transfer size) - largest possible link-level frame
  different link types, different MTUs
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…
25
hoant@uit.edu.vn

## Slide 26: IP fragmentation/reassembly
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…
26
hoant@uit.edu.vn
application transport network
link physical
Hn
M
segment
Ht
datagram
Hl
Hn Ht M
message
M
Ht
M
Hn Ht
frame
len(Ht)=20 bytes
len(Hn) = 20 bytes
MTU
max. transfer size
len(message)=MTU-40 bytes

## Slide 27: IP fragmentation/reassembly
 | length =4000 | ID =x | fragflag =0 | offset =0 |  |  | 
 | length =1040 | ID =x | fragflag =0 | offset =370 | 
 |  |  | length =1500 | ID =x | fragflag =1 | offset =0 |  |  | 
= |  | length | ID | fragflag | offset |  |  | 
 |  | =1500 | =x | =1 | =185 |  |  | 
Example
4000-byte datagram
MTU = 1500 bytes (1480 bytes + 20bytes Hn)
Length = 16 bits, ID = 3 bits, Flag = 3 bits, Fragment offset = 13 bits
one large datagram becomes several smaller datagrams
1480 bytes in data field (0-1479)
offset 1480/8
Why offset need to be devided by 8?
20 bytes Ht
20 bytes Hn
 = 40 bytes + app layer overhead for TCP+IP
1480 + 20
(0-1479)
1480 | 1480 | 1020
4000 -20=
1480 + 20
(1480-2959)
1020 + 20
(2960-3900)
Offset= the first byte of the fragment
https://datatracker.ietf.org/doc/html/rfc791
fragflag=0: terminal fragment
fragflag=1: other fragments follow

## Slide 28: Construct IP Fragments Manually Using Scapy
 | length = x | ID =y | fragflag =n | offset =n |  |  | 
frag = offset value
flags = fragment flag
ip.proto = 17: UDP
Execution Result
28

## Slide 29: Attacks Using IP Fragmentation Protocol Violation
Protocols Are Rules
 Attackers Like to Break Rules
 Robust Programs Handle Rule Violations

## Slide 30: Can you break the rules? Attacks Using IP Fragmentation
Q1: Can you create an IP packet that is larger than 65,536 bytes (64KB)?
  Super large package attacks!
Q2: Can you create some abnormal conditions using "offset" and "payload size"?
  Create abnormal situations attacks!
  Goal: Test whether a computer can handle these "unreal" conditions.
Q3: Can you use a small amount of bandwidth to tie up a target machine's significant amount of resources?
Tie Up Target's Resource attacks!

## Slide 31: Ping of Death (PoD) attack Attack 1: Create a Super-Large Packet
https://www.ionos.com/digitalguide/server/security/ping-of-death/
Q1: Can you create an IP packet that is larger than 65,536 bytes?  Violate the IP protocol  buffer overflow
 The Ping-of-Death Attack
ping packet = 64KBs ICMP = 65,536 bytes
ICMP data = 65536-20 -8= 65508
https://en.wikipedia.org/wiki/Ping_of_death

## Slide 32: Ping of Death (PoD) attack Attack 1: Create a Super-Large Packet
https://www.ionos.com/digitalguide/server/security/ping-of-death/
Q1: Can you create an IP packet that is larger than 65,536 bytes?  Violate the IP protocol  buffer overflow
 The Ping-of-Death Attack
ping packet = 64KBs ICMP = 65,536 bytes
ICMP data = 65536-20 -8= 65508

## Slide 33: Ping of Death (PoD) attack Attack 1: Create a Super-Large Packet
For example:
MTU=1500:
Number of fragments: ceiling(65508/1472)=45
Last fragment:
offset = ??
First 44 fragments: 44 x 1472 = 64768
20 | 8 | 1472
20 | 8 | 1000
Reassembled:64768 +1000=65 768 > 65 508
Dead!

## Slide 34: A Recent Ping of Death Vulnerability 1997’s vuln. is coming back!
How to mitigate PoD?
https://msrc.microsoft.com/update-guide/en-US/vulnerability/CVE-2020-16898
A remote code execution vulnerability exists when the Windows TCP/IP stack improperly handles ICMPv6 Router Advertisement packets, aka 'Windows TCP/IP Remote Code Execution Vulnerability'.

## Slide 35: CVE-2020-16898
[Windows TCP/IP Remote Code Execution vulnerability]
exploit proof-of-concept
October 13, 2020

## Slide 36: Teardrop Attacks Attack 2: Create Abnormal Situations
Q2: Can you create some abnormal conditions using "offset" and "payload size"?
Goal: Test whether a computer (A) can handle these "unreal" conditions.
 A cannot reassemble fragmented data packets
 the packets overlap one another, crashing the target network device.
H1 T1
T2
offset = 0
H2
offset = 600
length = 820
length = 820
H1
T1
H2
length = 820
T2
length = 420
offset = 0
offset =200
T2 – T1
 OK
T2 – T1 !!!
 negative  HUGE
unable to reassemble the packet, causing overload!
620!
820!

## Slide 37: Denial of Service Attack Attack 3: Tie Up Target's Resources
Packet 1
Packet 2
offset ~ 65535
Approach 1
(static buffer)
Approach 2
(linked list)
More complicated, time to implement!
Q3: Can you use a small amount of bandwidth to tie up a target machine's significant amount of resources?
 Send out 2 tiny packet ~ 100 bytes  tie up significant amount of resources on the server ~ 64KB
 Very efficient approach for DoS attack!
offset = 0
buffer = 64 KB

## Slide 38
NT101 – Network Security
Routing
and how to mitigate attacks

## Slide 39: Routing Scenario Network Topology
Internet
enp0s3
enp0s3
A
enp0s8
B
A wanna talk to B
 Will it work?

## Slide 40: Change routing table Linux routing
Add an IP Route entry $ sudo ip route add | 192.168.60.0/24 | dev | enp0s3 | via | 10.0.2.7
Delete an IP Route entry $ sudo ip route del | 192.168.60.0/24 |  |  |  | 
Show IP Route table $ ip route (route) |  |  |  |  | 

## Slide 41: Routing Rules Routing priority
Question: What interface will be used to route packets to (1) 192.200.60.5?
(2) 192.168.30.5?
(3) 192.168.60.5?
dev interface-a dev interface-b dev interface-a dev interface-d
default-route
A: 0.0.0.0/0
B: 192.168.0.0/16 C: 192.168.60.0/24 D: 192.168.60.5/32
Bottom line: Pick the longest match

## Slide 42: How Are Routing Tables Configured
Routing basis
For Routers
  Routing protocols (e.g. OSPF)
  Attacks on routing protocols (e.g. BGP) (will be discussed)
For Hosts (tiny routing table)
  DHCP (IP, DNS, router info.)
  Default routers
  Manual configuration (static route)
  ICMP redirect messages

## Slide 43: Reverse Path Filtering in Linux Kernel
Related term: Reverse-Path Forwarding (RPF)
Threat: Spoofing from outside network
(using internal src_ip  pretending to be inside)
 Cause damage
Router doesn’t want to do that! How?
IP address spoofing!
Reverse path filtering (rp_filter)
Check the source of the recived packet is reachable through the interface it came in
Packge is routable through the interface which it came: accept the packet
Packge is not routable through the interfxace: drop that packet.
Prevent IP address spoofing

## Slide 44: Reverse Path Filtering in Linux Kernel
Related term: Reverse-Path Forwarding (RPF)
Threat: Spoofing from outside network
(using internal src_ip  pretending to be inside)
 Cause damage
Router doesn’t want to do that! How?
Symmetric routing
  When R get a packet from interface A,
 do a reverse lookup, if the return path goes to the same interface?  OK = Allow
Otherwise, Asymmetric routing  Drop
!!! Very obscure and important rule inside the Linux Kernel, providing a level of protecting against packet spoofing
IP address spoofing!
packets are arriving from a legitimate path!

## Slide 45: IP Spoofing Demo - attack code

## Slide 46
NT101 – Network Security
ICMP Protocol
and Attacks

## Slide 47: ICMP: internet control message protocol
ICMP protocol
used by hosts and routers to communicate network-level information
  Error reporting: unreachable host, network, port, protocol, time exceeded
  Control messages:
    echo request/reply (used by ping)
    Redirect
    Timestamp request/reply
    Router advertisement/solicitation
ICMP messages carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error

## Slide 48
ICMP Header |  |  | 
ICMP header format |  |  | 
 | Type 0 | Code 0 | description echo reply (ping)
 | 3 | 0 | dest. network unreachable
 | 3 | 1 | dest host unreachable
 | 3 | 2 | dest protocol unreachable
 | 3 | 3 | dest port unreachable
 | 3 | 6 | dest network unknown
 | 3 | 7 | dest host unknown
 | 4 | 0 | source quench (congestion
 |  |  | control - not used)
 | 8 | 0 | echo request (ping)
 | 9 | 0 | route advertisement
 | 10 | 0 | router discovery
 | 11 | 0 | TTL expired
 | 12 | 0 | bad IP header

## Slide 49: ICMP Echo Request/Reply ICMP basis

## Slide 50: ICMP TTL Exceeded Time-to-live exceeded
TTL Max = 255,
Reduced by one before the node is routed onward

## Slide 51: ICMP Destination Unreachable Error detection

## Slide 52: ICMP Redirect Messages and Attacks ICMP Redirect
Attacker
 MITM Attack
ICMP redirect message = to inform a host of a more optimal route through a network
possibly used maliciously for attacks that redirect traffic to a specific node
LAN

## Slide 53: ICMP Redirect and Attacks Attack code
Execution Result

## Slide 54: Question: ICMP Redirect attacks
ICMP Attacks
Question 1: Can you launch ICMP redirect from a remote computer?
Question 2: Can you use ICMP redirect attacks to redirect to a remote computer?

## Slide 55: Question: ICMP Redirect attacks
ICMP Attacks
Question 1: Can you launch ICMP redirect from a remote computer?
Question 2: Can you use ICMP redirect attacks to redirect to a remote computer?
No! When A receiving ICMP Redirect, it will check the gateway is on the same network or not If not  ignore

## Slide 56: Question: ICMP Redirect attacks
ICMP Attacks
Question 1: Can you launch ICMP redirect from a remote computer?
No! Reverse path filtering (RPF) at the router will drop them!
Question 2: Can you use ICMP redirect attacks to redirect to a remote computer?
No! When A receiving ICMP Redirect, it will check the gateway is on the same network or not If not  ignore

## Slide 57: DoS Attacks strategies Analogy: A real war!
UDP DoS Attack (will be discussed later on!)

## Slide 58: Smurf Attack Attack ideas
https://www.imperva.com/learn/ddos/smurf-attack-ddos/
Spoofing source IP

## Slide 59: Smurf Attack Simple demo
What happened if we ping to the broadcast address?
How to prevent Smurf Attack?

## Slide 60: Various attacks using ICMP Other ICMP attacks
ICMP Flooding
Reconnaissance attack: gather all possible information about the target before launching an actual attack
https://www.cloudflare.com/learning/ddos/ping-icmp-flood-ddos-attack/

## Slide 61: Summary
What have we learned?
The Role of the IP layer
IP Header
IP Fragmentation and Attacks
Routing
ICMP and Attacks

## Slide 62: Homework Lab exercise
IP and ICMP Attacks Lab (Link)
  The objective of this lab is for students to gain the first-hand experience on various attacks at the IP layer.
  Working in a team (your final-project team) or individually.

## Slide 63: For next time…
Looking ahead
Ready for next class:
Tentative topic: Transport Layer and Attacks
Reading and practicing (in advance):
  SEED book, Chapter 16
    Refs: https://www.handsonsecurity.net/resources.html
  SEED Lab: TCP Attacks Lab and Mitnick Attack Lab
    Refs:
      https://seedsecuritylabs.org/Labs_16.04/Networking/TCP_Attacks/
      https://seedsecuritylabs.org/Labs_16.04/Networking/Mitnick_Attack/

## Slide 64
Today end,
Congrats!