## Slide 1: NT101-Network Security
Ngoc-Tu Nguyen, PhD
tunn@uit.edu.vn
Week 10-11: Transport Layer and Attacks

## Slide 2: Outline
Transport Layer (review)
UDP Protocol and attacks
  UDP Ping pong attacks
  UDP Flooding – DoS attacks
TCP Protocol and attacks
  TCP SYN Flooding
  TCP Reset Attack
  TCP Session Hijacking
  Reverse Shell
  The Mitnick Attack
Countermeasures

## Slide 3: Transport protocols (review)
mobile network
na P
local or regional ISP
home network co
pro
netwo er
enterprise
network
application
transport
network
data link
physical
application
transport
network
data link
physical
logical end-end transport
provide logical communication between application processes running on different hosts
transport protocols actions in end systems:
  sender: breaks application messages into segments, passes to network layer
  receiver: reassembles segments into messages, passes to application layer
transport protocols available to Internet applications
  TCP, UDP, QUIC (TCP/2)
https://datatracker.ietf.org/doc/html/rfc9000
Notes: QUIC =Quick UDP Internet Connections

## Slide 4: Transport Layer Actions
physical
link
network (IP)
application
physical
link
network (IP)
application
transport
Sender:
app. msg
is passed an application-layer message
determines segment header fields values
creates segment
passes segment to IP
transport
Th
Th
app. msg

## Slide 5: Transport Layer Actions
application
transport
network (IP) link
physical
application
transport
network (IP) link
physical
app. msg
Th
app. msg
Receiver:
receives segment from IP
checks header values
extracts application-layer message
demultiplexes message up to application via socket

## Slide 6: Port numbers
Overview
Port number: 16-bit unsigned numbers
Well-known ports: 0 – 1023
  Examples: ftp (20, 21), ssh (22), telnet (23), smtp (25), DNS (53), http (80), https (443)
  Super-user privilege needed: Why?
Less well-known ports: 1024 - 49151
  Examples: openVPN (1194), Microsoft SQL server (1433), Docker (2375-2377)
Private ports: 49152 - 65535 (2^16-1)
  Source ports

## Slide 7: Transport layer Protocols Overview
 | TCP | UDP
Connection | Connection-oriented Connection-less | 
Packet Boundary | Stream-based Maintain boundary | 
Reliability | ✅ ❌ | 
Ordering | ✅ ❌ | 
Speed | 🐢 slower 🐇 faster | 
Broadcast | ❌ ✅ | 
preserve application message
(during connection setup)

## Slide 8
UDP Protocol and Attacks
Transport Layer (review)
UDP Protocol and attacks
  UDP Ping pong attacks
  UDP Flooding – DoS attacks
TCP Protocol and attacks
  TCP SYN Flooding
  TCP Reset Attack
  TCP Session Hijacking
  Reverse Shell
  The Mitnick Attack
Countermeasures

## Slide 9: UDP segment header UDP header
application data (payload)
UDP segment format
32 bits
source port # dest port # length checksum
length, in bytes of UDP segment, including header
data to/from application layer

## Slide 10: Sending/Receiving UDP packets Python + Scapy
UDP Client example
UDP Server example

## Slide 11: UDP Applications
UDP Overview
DNS Protocol
Video/Audio Streaming, Skype, Zoom
  Note: Netflix and YouTube use UDP TCP, why?
Real-Time Applications
VPN Tunnel (OpenVPN)
Question
UDP does not preserve order and does not handle packet loss. If an application does care about packet loss and order, can it still use UDP?

## Slide 12: ICMP flood attack -DDoS (review)
need to reply!

## Slide 13: Smurf Attack (Review) Attack ideas
https://www.imperva.com/learn/ddos/smurf-attack-ddos/
Spoofing source IP

## Slide 14: UDP Ping-Pong Attacks
UDP Attacks
Some service or application issues a UDP reply no matter what is the input packet:
    Daytime protocol (port 13)
    Time Protocol (port 37)
    Echo Protocol (port 7)
    Character Generator Protocol - chargen (port 19)
 This causes a Ping-Pong effect between the source and the destination  DDoS attack (Smurf Attack ).

## Slide 15: Ping-Pong attack
need to reply!
UDP (src_port, dst_port = 7)
Reply …
UDP (src_port, dst_port = 7)
Reply …
Botnet?
13, 19, 37 …

## Slide 16: UDP flood attack Attack ideas
https://www.imperva.com/learn/ddos/smurf-attack-ddos/
Spoofing source IP
Reply …
UDP (src_port, dst_port = 7)
13, 19, 37 …
Reply with large package?

## Slide 17: Let's Bring the Ping-Pong Game Back!
UDP Attacks
Server code
Attack code
Triggering UDP Ping Pong (spoofing)

## Slide 18: Ping-pong demo UDP Attacks

## Slide 19: DoS Attack strategies Recall
UDP DoS Attack
ICMP Smurf Attack
hoant@uit.edu.vn

## Slide 20: UDP Amplification Attack
UDP Attack
Idea: Applications that reply with large packets to small requests, e.g., games
  BattleField 1942
  Quake 1,2,3 (CAN-1999-1066)
  Unreal Tournament
Hosts can be attacked by using these applications as amplifiers, with forged source IP packets
The ratio between the response and the original request pack is called amplification ratio.
https://www.christian-rossow.de/articles/Amplification_DDoS.php
20

## Slide 21: Bandwidth Amplification Factor UDP Attack
UDP Attacks - Bottom line:
The more complicated a protocol is, the more
sophisticated attack that you can create.
https://www.christian-rossow.de/articles/Amplification_DDoS.php
21

## Slide 22
TCP Protocol and Attacks

## Slide 23: TCP Protocol
TCP Overview
Transmission Control Protocol (TCP) is a core protocol of the Internet protocol suite.
Sits on the top of the IP layer; transport layer.
Provide host-to-host communication services for applications.
The Need for TCP
  Providing a Virtual Connection
  Maintaining Order
  Reliability
  Flow Control
Recall: Two transport Layer protocols
  TCP: provides a reliable and ordered communication channel between applications.
  UDP: lightweight protocol with lower overhead and can be used for applications that do not require reliability or communication order.
SEED lectures

## Slide 24: TCP Client Program
TCP overview
Create a socket; specify the type of communication. TCP uses SOCK_STREAM and UDP uses SOCK_DGRAM.
Initiate the TCP connection
Send data

## Slide 25: TCP Server Program (cont.) TCP Overview
Step 1 : Create a socket. Same as Client Program.
Step 2 : Bind to a port number. An application that communicates with others over the network needs to register a port number on its host computer. When the packet arrives, the operating system knows which application is the receiver based on the port number. The server needs to tell the OS which port it is using. This is done via the bind() system call

## Slide 26: TCP Server Program (cont.) TCP Overview
Step 3 : Listen for connections.
After the socket is set up, TCP programs call listen() to wait for connections.
It tells the system that it is ready to receive connection requests.
Once a connection request is received, the operating system will go through the 3-way handshake to establish the connection.
The established connection is placed in the queue, waiting for the application to take it.
The second argument (5) gives the number of connection that can be stored in the queue.

## Slide 27: TCP Server Program (cont.) TCP Overview
Step 4: Accept a connection request
After the connection is established, an application needs to “accept” the connection before being able to access it. The accept() system call extracts the first connection request from the queue, creates a new socket, and returns the file descriptor referring to the socket.
Step 5 : Send and Receive data
Once a connection is established and accepted, both sides can send and receive data using this new socket.

## Slide 28: Improved TCP Server Program
fork() system call creates a new process by duplicating the calling process.
On success, the process ID of the child process is returned in the parent process and 0 in the child process.
Line ! and Line " executes child and parent process respectively.
TCP Overview
To accept multiple connections :

## Slide 29: TCP Data Transmission (cont.) Send/Receive buffers
Once a connection is established, OS allocates two buffers at each end, one for sending data (send buffer) and receiving buffer (receive buffer).
When an application needs to send data out, it places data into the TCP send buffer.

## Slide 31: TCP Data Transmission (cont.) Send/Receive buffers
Each octet in the send buffer has a sequence number field in the header which indicates the sequence of the packets. At the receiver end, these sequence numbers are used to place data in the right position inside receive buffer.
Once data is placed in the receive buffer, they are merged into a single data stream.
Applications read from the receive buffer. If no data is available, it typically gets blocked. It gets unblocked when there is enough data to read.
The receiver informs the sender about receiving of data using acknowledgement packets
Question: If two programs on the same machine send data to the same TCP server on another machine, would the server mix their data? What if the server is a UDP server?

## Slide 32: Connection-oriented demultiplexing: example
application P1 |  |  |  | 
transport |  |  |  | 
network |  |  |  | 
link |  |  |  | 
physical |  |  |  | 
transport
application
physical
link
P4
transport
physical
link
network
host: IP address A
host: IP address C
network
P6
P5
application
P2 P3
source IP,port: A,9157 dest IP, port: B,80
source IP,port: B,80 dest IP,port: A,9157
source IP,port: C,5775 dest IP,port: B,80
source IP,port: C,9157 dest IP,port: B,80
server: IP address B
Three segments, all destined to IP address: B,
dest port: 80 are demultiplexed to different sockets

## Slide 33: Connectionless demultiplexing: an example
DatagramSocket serverSocket = new DatagramSocket
(6428);
transport
physical
link
network
application
P3
transport
physical
link
network
application
P1
transport
physical
link
network
application
P4
DatagramSocket mySocket1 = new DatagramSocket (5775);
DatagramSocket mySocket2 = new DatagramSocket
(9157);
source port: 9157
dest port: 6428
source port: 6428
dest port: 9157
source port: ? dest port: ?
source port: ? dest port: ?

## Slide 34: TCP Header TCP overview
TCP Segment = TCP Header + Data.
Source and Destination port (16 bits each): Specify port numbers of the sender and the receiver.
Sequence number (32 bits) : Specifies the sequence number of the first octet in the TCP segment. If SYN bit is set, it is the initial sequence number.
Acknowledgement number (32 bits): Contains the value of the next sequence number expected by the sender of this segment. Valid only if ACK bit is set.

## Slide 35: TCP Header
TCP overview
Header length (4 bits): Length of TCP header is measured by the number of 32-bit words in the header, so we multiply by 4 to get number of octets in the header.
Reserved (6 bits): This field is not used.
Code bits (6 bits): There are six code bits, including SYN,FIN,ACK,RST,PSH and URG.
Window (16 bits): Window advertisement to specify the number of octets that the sender of this TCP segment is willing to accept. The purpose of this field is for flow control.
Checksum (16 bits): The checksum is calculated using part of IP header, TCP header and TCP data.
Urgent Pointer (16 bits): If the URG code bit is set, the first part of the data contains urgent data (do not consume sequence numbers). The urgent pointer specifies where the urgent data ends and the normal TCP data starts. Urgent data is for priority purposes as they do not wait in line in the receive buffer, and will be delivered to the applications immediately.
Options (0-320 bits, divisible by 32): TCP segments can carry a variable length of options which provide a way to deal with the limitations of the original header.

## Slide 36: TCP 3-way Handshake Protocol TCP overview
SYN Packet:
The client sends a special packet called SYN packet to the server using a randomly generated number x as its sequence number.
SYN-ACK Packet:
  On receiving it, the server sends a reply packet
using its own randomly generated number y as its sequence number.
ACK Packet
  Client sends out ACK packet to conclude the handshake
Notes: SYN seq= x = (random number)
SYN seq = y = (random number)

## Slide 37: TCP 3-way Handshake Protocol TCP overview
When the server receives the initial SYN packet, it uses TCB (Transmission Control Block) to store the information about the connection.
This is called half-open connection as only client-server connection is confirmed.
The server stores the TCB in a queue that is only for the half-open connection.
After the server gets ACK packet, it will take this TCB out of the queue and store in a different place.
If ACK doesn’t arrive, the server will resend SYN+ACK packet. The TCB will eventually be discarded after a certain time period.

## Slide 38: SYN Flooding Attack (cont.)
TCP Attacks
Idea: To fill the queue storing the half-open connections so that there will be no space to store TCB for any new half-open connection, basically the server cannot accept any new SYN packets.
Steps to achieve this: Continuously send a lot of SYN packets to the server. This consumes the space in the queue by inserting the TCB record.
Do not finish the 3rd step of handshake as it will dequeue the TCB record.

## Slide 39: SYN Flooding Attack TCP Attacks
When flooding the server with SYN packets, we need to use random source IP addresses; otherwise the attacks may be blocked by the firewalls.
The SYN+ACK packets sent by the server may be dropped because forged IP address may not be assigned to any machine.
If it does reach an existing machine, a RST packet will be sent out, and the TCB will be dequeued.
  As the second option is less likely to happen, TCB records will mostly stay in the queue. This causes SYN Flooding Attack.

## Slide 40: Launching SYN Flooding Attack: Before Attacking TCP Attacks
TCP States
LISTEN: waiting for TCP connection.
ESTABLISHED: completed 3-way handshake
SYN_RECV: half-open connections
Check the TCP states

## Slide 41: SYN Flooding Attack – Launch the Attack
Using netwox tool
Turn off the SYN Cookie countermeasure:
$sudo sysctl -w net.ipv4.tcp_syncookies=0
Result
Targeting telnet server
Launch the attack using netwox
$ sudo netwox 76 -i 10.102.20.178 -p 23 -s raw

## Slide 43: SYN Flooding Attack - Launch with Spoofing Code
Using C
We can write our own code to spoof IP SYN packets.

## Slide 44: SYN Flooding Attack - Launch with Spoofing Code Using Scapy

## Slide 45: SYN Flooding Attack Results
Using netstat command, we can see that there are a large number of half-open connections on port 23 with random source IPs.
Using top command, we can see that CPU usage is not high on the server machine. The server is alive and can perform other functions normally, but cannot accept telnet connections only.

## Slide 46: SYN Cookies
https://en.wikipedia.org/wiki/SYN_cookies
Countermeasures
If it is getting filled up quickly the think cookie will kick in now when the thin cookie kick in
After a server receives a SYN packet, it calculates a keyed hash (H) from the information in the packet using a secret key that is only known to the server.
This hash (H) is sent to the client as the initial sequence number from the server. H is called SYN cookie.
The server will not store the half-open connection in its queue.
  If the client is an attacker, H will not reach the attacker.
  If the client is not an attacker, it sends H+1 in the acknowledgement field.
The server checks if the number in the acknowledgement field is valid or not by recalculating the cookie.
🏡 Homework: Find out how SYN cookies work in detail

## Slide 47: TCP Reset Attack How to close TCP connections?
To disconnect a TCP connection :
A sends out a “FIN” packet to B.
B replies with an “ACK” packet. This closes the A- to-B communication.
Now, B sends a “FIN” packet to A and A replies with “ACK”.
Using Reset flag :
One of the parties sends RST packet to immediately break the connection.
  Don’t need to wait ACK

## Slide 48: TCP Reset Attack TCP Attacks
Goal: To break up a TCP connection between A and B.
Spoofed RST Packet: The following fields need to be set correctly:
Source IP address, Source Port,
Destination IP address, Destination Port
Sequence number (within the receiver’s window)

## Slide 49: Captured TCP Connection Data How to get the Sequence number?
Steps :
Use Wireshark on attacker machine, to sniff the traffic.
Retrieve the destination port (23), Source port number and sequence number.
How to get the seq# automatically?

## Slide 50: TCP Reset Attack on Telnet Connection TCP Attacks

## Slide 52: TCP Reset Attack on SSH connections TCP Attacks
If the encryption is done at the network layer, the entire TCP packet including the header is encrypted, which makes sniffing or spoofing impossible.
But as SSH conducts encryption at Transport layer, the TCP header remains unencrypted. Hence the attack is successful as only header is required for RST packet.

## Slide 53: TCP Reset Attack on Video-Streaming Connections
TCP Attacks
This attack is similar to previous attacks only with the difference in the sequence numbers as in this case, the sequence numbers increase very fast unlike in Telnet attack as we are not typing anything in the terminal.
To achieve this, we use Netwox 78 tool to reset each packet that comes from the user machine (10.0.2.18). If the user is watching a Youtube video, any request from the user machine will be responded with a RST packet.

## Slide 54: TCP Reset Attack on Video-Streaming Connections TCP Attacks
Note: If RST packets are sent continuously to a server, the behavior is suspicious and may trigger some punitive actions taken against the user.

## Slide 55: TCP Session Hijacking Attack TCP Attacks
Goal: To inject data in an established connection.
Spoofed TCP Packet: The following fields need to be set correctly:
Source IP address, Source Port,
Destination IP address, Destination Port
Sequence number (within the receiver’s window)

## Slide 56: TCP Session Hijacking Attack: Sequence Number
TCP Attacks
If the receiver has already received some data up to the sequence number x, the next sequence number is x+1. If the spoofed packet uses sequence number as x+𝛿, it becomes out of order.
The data in this packet will be stored in the receiver’s buffer at position x+𝛿, leaving 𝛿
spaces (having no effect). If 𝛿 is large, it may fall out of the boundary.

## Slide 57: Hijacking a Telnet Connection
Steps:
User establishes a telnet connection with the server.
Use Wireshark on attacker machine to sniff the traffic
Retrieve the destination port (23), source port number (46712) and sequence number.
TCP Attacks
With Next Sequence Number
Without Next Sequence Number

## Slide 58: What Command Do We Want to Run
TCP Attacks
By hijacking a Telnet connection, we can run an arbitrary command on the server, but
what command do we want to run?
Consider there is a top-secret file in the user’s account on Server called “secret”. If the attacker uses “cat” command, the results will be displayed on server’s machine, not on the attacker’s machine.
In order to get the secret, we run a TCP server program so that we can send the secret from the server machine to attacker’s machine.

## Slide 59: Session Hijacking: Steal a Secret
TCP Attacks
“cat” command prints out the content of the secret file, but instead of printing it out locally, it redirects the output to a file called /dev/tcp/10.0.2.16/9090 (virtual file in /dev folder which contains device files). This invokes a pseudo device which creates a connection with the TCP server listening on port 9090 of 10.0.2.16 and sends data via the connection.
The listening server on the attacker machine will get the content of the file.

## Slide 60: Launch the TCP Session Hijacking Attack TCP Attacks
Client
 Freeze
Attacker

## Slide 61: What Happens to The Session? TCP Attacks
Once the attack is successful, telnet connection freezes. It can no longer be used. What happened?
 Both user and server have entered the deadlock

## Slide 62: Creating Reverse shell
TCP Attacks
The best command to run after having hijacked the connection is to run a reverse shell command.
To run shell program such as /bin/bash on Server and use input/output devices that can be controlled by the attackers.
The shell program uses one end of the TCP connection for its input/output and the other end of the connection is controlled by the attacker machine.
Reverse shell is a shell process running on a remote machine connecting back to the attacker.
  It is a very common technique used in hacking.

## Slide 63: File Descriptors and Standard IO File descriptor table
File descriptor 0 represents the standard input device (stdin)
File descriptor 1 represents the standard output device (stdout)
File descriptor 2 represents the standard error (stderr).
> write permission
< read permission
& redirect

## Slide 64: Reverse Shell TCP Reverse Shell
File descriptor 0 represents the standard input device (stdin) and 1 represents the standard output device (stdout). Since the stdout is already redirected to the TCP connection, this option basically indicates that the shell program will get its input from the same TCP connection.
File descriptor 2 represents the standard error (stderr). This cases the error output to be redirected to stdout, which is the TCP connection.
The option i stands for interactive, meaning that the shell should be interactive.
This causes the output device (stdout) of the shell to be redirected to the TCP connection to 10.0.2.70’s port 9090.

## Slide 65: TCP Hijacking with Reverse Shell Demo
Attacker machine
Client (telnet to Server – 178)
Successful!

## Slide 66: Defending Against Session Hijacking
Randomize source port number (16 bits)
Randomize initial sequence number (32 bits)
* Not effective against local attacks
Encrypting payload
  Attackers need to know how the data is encrypted  the encryption key
 Encryption is one of the fundamental solutions to many of the attacks on the Internet.
Countermeasures
Making it difficult for attackers to spoof packets
 Guest a random 48-bit number !!!

## Slide 67: Summary
TCP protocol
Three-way handshake protocol
TCP Attacks
  SYN flooding attack
  TCP reset attack
  TCP session hijacking attack
  The Mitnick attack
Reverse shell
Countermeasures
What have we learned?
Transport layer
UDP Protocol
UDP Attacks
  UDP Ping pong attacks
  UDP Flooding – DoS attacks

## Slide 68: Homework (Bonus points ) Lab exercise
Lab 1: TCP Attack Lab (Link)
  The learning objective of this lab is for students to gain first-hand experience on three types of attacks on TCP, including the SYN flooding attack, TCP reset attack, and TCP session hijacking attack.
Lab 2: The Mitnick Attack Lab (Link)
  (optional with .ATCL class, mandatory with .ANTN class)
  The objective of this lab is to recreate the classic Mitnick attack, so students can gain the first-hand experience on such an attack. We will emulate the settings that was originally on Shimomura's computers, and then launch the Mitnick attack to create a forged TCP session between two of Shimomura's computers. If the attack is successful, we should be able to run any command on Shimomura's computer.

## Slide 69: For next time…
Looking ahead
Ready for next class:
Tentative topic: Application layer, DNS and Attacks
Reading and practicing (in advance):
  SEED book, Chapter 18
    Refs: https://www.handsonsecurity.net/resources.html
  SEED Lab: Local DNS Attack Lab, Remote DNS Attack Lab and DNS Rebinding Attack Lab
    Refs:
      https://seedsecuritylabs.org/Labs_16.04/Networking/DNS_Local/
      https://seedsecuritylabs.org/Labs_16.04/Networking/DNS_Remote/
      https://seedsecuritylabs.org/Labs_16.04/Networking/DNS_Rebinding/

## Slide 70
Today end,
Congrats!